## Slide 2: TCA Manufacturing
Adaptive Robotics Laboratory

## Slide 3: Twisted Coil Actuator
Materials:
Conductive Nylon thread
  PN#200121235364HCB
  235/36 dtex 4 ply HCB
  V Technical Textiles, Inc.
26 ga copper wire (core)
32 ga copper wire (guide channel)
Useful information:
Anneal 2 hours at 185° C
Use “Step Calculator” in Parts List TCA Machine excel sheet to adjust lengths
For “Type i” TCA
  Natural thread length for full size TCA is 3.6 m
  Twist 2160 times (216,000 steps/ motor)

## Slide 4: STEPS
Cut 26 ga wire (core) to desired length and twist loops in each end.
Connect to top and bottom mandrel motors (locate on the left side).
Twist loop in 32 ga (guide) wire, attach to the same side hook as the core wire and unwind approximately 3x the length of the 26 core wire.
Run 32 ga guide wire through lower pulley and tighten spool on top of machine (ensure proper mass is on lower pulley mounting plate).
At MEDIUM speed, use MANDREL ONLY function to secure guide wire to core and position it to insert into the follower guide.
With guide wire in guide and tensioner rubber bands on, at the SECOND TO HIGHEST speed, press COIL button and closely monitor the traveler, manually stop at bottom of the TCA.
Use MANDREL ONLY function to secure guide wire to core, then cut and tie off guide wire.
Remove mandrel from top motor and place on side hook.
Home travelers using HOME TRAVELERS button.
Cut thread to length (depending on helical angle / desired TCA length) and tie loops on each end.
Connect to left and right top motor hooks, running through lower pulley (ensure proper mass is on lower pulley mounting plate).
On HIGH speed, press TWIST button (remember to turn off button when operation is complete!)
Replace top of mandrel to the top motor on the opposite side hook as twisted thread.
Repeat steps 6-8 to coil and secure both ends of twisted thread to mandrel.
Remove TCA from lower hook and twist a loop in the end to “lock” thread. Repeat with top.
Home travelers using HOME TRAVELERS button.
Anneal in the oven for 2 hours at 185° C.
Untwist loops and cut guide wire and begin to manually unwind it at the top of the TCA.
Attach to mandrel motors and while holding the unwound end of the guide wire, at MEDIUM speed push MANDREL ONLY button to unwind guide wire.
Remove from machine, cut ends and pull mandrel core out of TCA.

## Slide 5
Updated code for the TCA machine can be found here:
https://github.com/bztighe/Arduino-Code/tree/master/TCA%20Machine
Additional resources including Excel book with parts list, wiring diagrams, length/ step calculator, etc:
https://drive.google.com/drive/folders/1GMNalh82XPEKqc4Yx6E1d4W8H_9g_3dO
More information about Dr. Jianguo Zhao and the Adaptive Robotic Laboratory can be found here:
https://www.engr.colostate.edu/~zhao/
All of the content of this video is property of Dr. Jianguo Zhao and the Adaptive Robotics Laboratory at Colorado State University. Unauthorized use, replication, or distribution of this video or any of the content therein without direct and written consent from its owner is strictly prohibited.